BUZZER Driver for AVR Microcontrollers

Version: 1st Date: 26/10/2023
API specification
       1.1 Type definitions

Name:	BUZZER_config_t
Type:	STRUCT
Element:	DIO_PIN_ID pin_id; / DIO_PORT_ID port_id; / DIO_PIN_DIRECTION_TYPE pin_direction;,
Description:	Type definition for a BUZZWE configuration.

2. Function definitions
Service name:	BUZZER_init
Syntax:	void BUZZER_init(BUZZER_config_t *buzzer_config);
Parameters (in):	BUZZER_config_t *buzzer_config
Parameters (in/out):	None
Parameters (out):	None
Return value:	None
Description:	1. Fill the BUZZER configurations structure / 2. Set the PIN direction which the led is connected as OUTPUT pin / 3. Initialize the BUZZER ON/OFF according to the initial value
NUM:

Service name:	BUZZER_setOn
Syntax:	void BUZZER_setOn(void)
Parameters (in):	None
Parameters (in/out):	None
Parameters (out):	None
Return value:	None
Description:	Description: Set the BUZZER state to ON
NUM:

Service name:	BUZZER_setOff
Syntax:	void BUZZER_setOff(void);
Parameters (in):	None
Parameters (in/out):	None
Parameters (out):	None
Return value:	None
Description:	Description: Set the BUZZER state to OFF
NUM: